15

14

13

12

11

10

9

8

7

6

5

4

3

2

1

| Total | Share factor | Wight | Quantity | Part | Source | Ser. |
| --- | --- | --- | --- | --- | --- | --- |
| 400 | 1 | 40 | 10 | 10F | post | 1 |
| 16 | 1 | 16 | 1 | 4F | Post | 2 |
| 200 | 0.5 | 20 | 20 | 5F | Bearer | 3 |
| 224 | 0.5 | 32 | 14 | 8F | zigzag | 4 |
| 60 | 1 | 3 | 20 | ------ | right angle clamp | 5 |
| 56 | 1 | 4 | 13 | ------ | swivel clamp | 6 |
| 20 | 0.5 | 20 | 2 | 4F | Toe board | 7 |
| 320 | 0.5 | 32 | 20 | 8F | Runner for front view | 8 |
| 60 | 1 | 3 | 20 | ------ | right angle clamp for front view | 9 |
| 35 | 0.5 | 35 | 2 | 8F | Toe board for front view | 10 |
| 56 | 1 | 4 | 13 | ------ | Swivel joint clamp | 11 |
| 280 | 0.5 | 40 | 14 | 10F | Face bracing | 12 |

After we finish all of above calculation  we must calculate the last item

___________________________________________________

Wood =

number of parts x  length  x Wight per feet  x number of levels x 0.25

___________________________________________________________

Wood =

4                x      8       x      25           x         10             x 0.25

2000 lb.	=

Dead load =

Total of the above table + wood Weight

Dead load =

400+16+200+224+60+56+20+320+60+35+56+280+2000

=3727

Live load

Platform area     x   load /feet2   / 4   x   2

4 x 7                 x    25    / 4    x   2 =   350 p

Maximum intended load of that scaffold

Live load   + Dead load

= 3727       +      350   =

4077 lb.

# Text boxes

TO calculate the dead Weight Of scaffold we must be aware of all scaffold components as follows :-

1- posts -   (vertical    Pipe )

2- Bearers - (horizontal pipe perpendicular to the building structure

3- Transverse braces  -   pipe  which take a diagonal shape  when used

4- Right angle clamps

5- Swivel joint clamps

6- Toe boards

7- Runners

8 - Face bracing

And    now  you can search   about   the  data   which you can use   it in  scaffold building  and then you can calculate the live load and  add it to the dead load  to know  the maximum intended  load in this scaffold per single leg.

مسقط راسى

مسقط امامى

مسقط  جانبى