Scaffolding

Some things to know before you give your talk.

As a Team Leader, you should know that over one-third of the serious injuries to workers in the construction industry are caused by falls from one level to another.  These accidents usually occur because someone is working or standing on an unsafe surface (a makeshift scaffold) or using a scaffold incorrectly or working on one that hasn't been put up properly.  They may seem safe but they can be very dangerous.  Makeshift scaffolds should not be used and are made of such things as:

• Drums

• Boxes

• Buckets

• Piles of scrap material

• Poorly supported wooden planks

• Machinery

Take the time to build a safe scaffold by using the correct scaffold material.  We are not in such a hurry that we are willing to sacrifice safety.  There are a couple kinds of scaffolds that are acceptable if built right.  Some examples of scaffolds and things to remember when erecting them are:

Rolling Scaffold (occasionally used offshore)

• They should only be used on a level surface.

• The height should not exceed 3 times the minimum base dimension, unless guyed or equipped with outriggers.

• Decking should be full width and secured against displacement.

• They should have guardrails, midrails and toeboards.

• All casters should be locked except when the scaffold is being moved.

• No one should be on it while it is being moved.

• Tubular Metal Scaffold

• Should be tied to and braced against the structure at intervals not to exceed 30 feet horizontally and 26 feet vertically.

• They should have guardrails, midrails and toe boards.

• Screwjacks should be adjusted to plumb and level the scaffold.

• All cross bracing should be installed.

• Planks should be lapped not less than 12" or more than 18".

• Safe means of access should be provided - Climbing cross bracing is

Dangerous.

- Base plates must be used

Try this for show and tell!

Look at some job site scaffolds and talk about what is right about them and what is wrong.

Questions you can use to get them talking:

• Have you seen any makeshift scaffolds on this job?  Where?

• Why do we see so many makeshift scaffolds on construction jobs?

• Has anyone ever had an accident—or know of one—involving a makeshift scaffold?