Scaffolding

Name :………………………………………..Dep.:……  ………………..Date:………….

A- Choose the correct answer “Some question may have more than correct answer”

1- The top Rail for the scaffolding platform must be not less than

- 40 Inch

- 42 Inch

- 43 Inch

2- The toe-board for the scaffolding platform must be not less than

- 4 Inch

- 5 Inch

- 6 Inch

3-We must use the fixed ladders when the scaffolding high more than

  - 12 Feet

  - 14 Feet

  - 16 Feet

4- We must use Fall Protection method when the high of the scaffolding more than

- 14 Feet

- 12 Feet

- 10 Feet

5-  We must leave distance between the scaffolding and  electric wire not less than

- 14 Feet

- 12 Feet

- 10 Feet

6- For pending scaffolding the safety rope must load ……. The scaffolding weigh and any thing over it .

- 6 time

- 7 time

- 8 time

7- We must tie the scaffolding when it’s high more than……. From it’s wide

- 4 time

- 6 time

- 8 time

8-  There is …… kind of scaffolding ties

- 3

- 4

- 5

9- We can classified the scaffolding for it’s load to …….. kind

- 3

- 4

- 5

10-  The overlap distance for the wooden sheet using in scaffolding platform must be not less than

- 4 Inch

- 5 Inch

- 6 Inch

أختبار فنين السقالات

الاسم : ........................................................... المهنة : .......................... التاريخ  : ……………...............

اختر الإجابة الصحيحة

- -1 يجب أن يكون الحاجز العلوى لمنصة السقالات لا تقل عن

- 40 بوصة (100 سم )

- 42 بوصة  (105 سم)

- 43 بوصة (107.5 سم )

2- يجب أن يكون حاجز القدم لمنصة السقالات لا تقل عن

- 4 بوصة (10 سم )

- 5 بوصة  (12.5 سم)

- 6 بوصة (15 سم)

3- يجب استخدام سلالم ثابتة عند السقالات العالية أكثر من

- 12 قدم ( 3.6 متر)

- 14 قدم (4.2 متر)

- 16 قدم  (4.8 متر)

4- يجب أن نستخدم أسلوب حماية عندما تعلو السقالات أكثر من

- 14 قدم ( 4.2 متر )

- 12 قدم ( 3.6 متر)

- 10 قدم (3 متر)

5- يجب أن نترك مسافة بين السقالات و الأسلاك الكهربائية لا تقل عن

- 14 قدم ( 4.2 متر )

- 12 قدم ( 3.6 متر)

- 10 قدم (3 متر)

-6 معامل أمان ويرات السلامة المستخدمة فى  السقالات المعلقة

      - 6  مرة

- 7 مرة

- 8  مرة

7 - يجب علينا ربط السقالات عندما يكون ارتفاع أكثر من ....... عرضها (اصغر ضلع فى القاعدة)

- 4 مرة

- 6 مرة

- 8  مرة

- 8 هناك عدد........... انواع لربط السقالات

- 3

- 4

- 5

9 - يمكننا تصنيف سقالات حسب قدرة التحمل الـ ............ نوع

- 3

- 4

- 5

- 10يجب أن تكون اقصى مسافة بروز الألواح الخشبية عن المنصة...........

- 4 بوصة (10 سم)

- 5 بوصة (12.5 سم)

- 6 بوصة (15 سم)