Hse&e Self – Assessment Checklist – SCAFFOLDS

Date of Inspection :- (… … / … … / … … … …) Time of Inspection :- (… …: … …) Project Name: - _______________________________ Project No. :- (… … … … … …) Project Location: - ____________________________ Scaffold No. :- (… … … … … …) Scaffold Location :- ____________________________ Auditor: - _____________________

Check "Yes" if an assessment item is complete / correct. Check "No" if an item is incomplete / deficient. Deficiencies shall be brought to the immediate of the scaffold subcontractor. Section 3 must be completed for all items checked "No". Check "N/A" if an item is not applicable. Check "N/O" if an item is applicable but was not observed during the assessment.

SECTION 1:- PERSONNEL SAFE WORK PRACTICES

Competent person has completed work shift inspection and has authorized scaffold access Personnel aware of and following access requirements established by competent person Scaffold free from damage and in stable condition Safe means of access provided to scaffold platform Personnel remaining within guardrail system when provided Personnel using personal fall arrest system (PFAS) when required Personnel working from suspension scaffold or boatswains ,chairs using (PFAS) Have completed fall protection training when (PFAS) use required Personnel not standing on objects or ladders on top of scaffold platforms Personnel not using ladders on top of scaffold platforms unless platform covers the entire floor Personnel not working on scaffold covered with snow or ice Personnel not work on scaffold during storm / high winds unless adequate protection provided

SECTION 2:- General

.scaffold inspected by competent before each work shift 14.damaged or workend scaffold components immediately repaired or replaced 15.scaffold not loaded in excess of their maximum intended load 16. Debris is not accumulating on scaffold platforms Assembly/ disassembly of scaffolds ( 3.2.1 ) 17. Scaffold designed by qualified person 18. Scaffold assembled / disassembled by experienced and trained personnel 19.scaffold assembled / disassembled under supervision and direction of competent person 20. Adequate planking provided ,as determined by competent person 21. Adequate safe means of access provided , as determined by competent person 22. Adequate fall protection provided , as determined by competent person Scaffold construction( 3.2.1 ) 23. Scaffold capable of supporting own weight and 4 times maximum intended load 24. Compatible scaffold components used 25. Scaffold uprights bear on stable foundations 26. Scaffold adequately braced to prevent racking / collapse 27. Scaffold plump, level , and squared 28. Scaffold with height to width ratios greater than 4:1 secred from tipping 29. Work plat forms fully planked or decked 30. Platform planking extended over supports appropriate amount or restrained 31. Safe means of access is provided to platforms 32. Supported scaffold>3m provided with guardrails or peas 33. When required , adequate guardrail system installed on all plat form open sides an ends 34. When required ,adequate peas provided ( may also use fall protection checklist hs31) 35. Falling object protection provided to personnel working on scaffold /under scaffold 36. Safe clearance maintained from overhead power lines Mobile scaffold ( 3.2.1 ) 37. Casters/ wheels locked while scaffold used in the stationary position 38. Personnel not riding mobile scaffold unless safe to move Suspension scaffolds ( 3.2.1 ) 39. Suspension scaffolds and boatswains, chairs>3 m provided with personal fall arrest system 40. Supporting devices / counterweights secured to supporting structure 41. Supporting devices inspected by competent person prior to scaffold use 42. Ropes and connecting hardware capable of supporting 6 times the maximum intended load 43. Suspension ropes inspected by competent person before each work shift 44. Damaged or repaired wire rope not used suspension rope 45. Suspension ropes joined together only by eye splice thimbles connected by shackles 46. Wire rope clips inspected / retightened after initial loading and before each work shift 47. Scaffold ropes protected from welding , heat , and corrosives 48. Scaffold tide or otherwise secured from swaying Adjustable suspension scaffold ( 3.2.1 ) 49. Adjustable suspension scaffold > 3mprovided with guardrails and peas 50. Supporting structures capable of resisting tipping moment 51. Hoist ropes restrained from passing through the hoist 52. Hoists have braking device / locking paw 1 that engages during scaffold uncontrolled movements 53. Manually operated hoists require positive crank force to lower 54. Scaffold hoist stall load less than 3 times its rated load 55. Gasoline – powered hoists not use

h&S SELF – ASSESSMENT CHECKLIST – SCAFFOLDS

Section 3 Complete this section for all items checked 'no' in section 1 or 2 deficient items must be corrected in timely manner.

| Date corrected | Corrective action planned / taken | Item# |
| --- | --- | --- |

Auditor------------------------------------------------------------ project manager ----------------------------------