Crane Operators Check List

| Component | Action |  | Response |
| --- | --- | --- | --- |
| Access Ladders, | free from obstruction cleaned of any residual oils and greases |  |  |
| Walkways and Hatches | all deck plates are secured access hatches closed |  |  |
| Hoses | Service hoses, e.g., diesel, air, and water are neatly stowed |  |  |
| Signs | Warning signs and barriers are posted accordingly |  |  |
| Pre-start Checks | Carry out a visual check of the crane to determine its serviceability |  |  |
|  | the boom, look for bent or damaged struts |  |  |
|  | hook blocks, sheaves |  |  |
|  | wire ropes and pendants correct spooling on drums and rope terminations |  |  |
|  | any anchorage points |  |  |
|  | Check that cladding and panel work in crane operations cab and Machinery House is watertight in order to prevent water ingress which may affect the operational integrity of the crane |  |  |
|  | A physical check of all oil levels, coolant level and fuel level. |  |  |
|  | Check that all guards over and around moving machinery are in place and secure |  |  |
|  | Check machinery house is in a clean and tidy condition. Clean up any oil spillages and remove any loose materials, e.g. tools, rags |  |  |
|  | Ensure that all personal belongings or clothing are stored in such a manner that they do not interfere with the proper control of the crane during operations |  |  |
| Start-up (Prime Mover) | Prior to start-up, ensure that all controls are in neutral position and that the main clutch (where fitted) is disengaged |  |  |
|  | On start-up of prime mover, ensure that all air and oil pressure gauges are within safe operating range before carrying out function check of the crane controls. |  |  |
|  | Carry out function check of all crane controls at the commencement of each shift. On friction clutch and brake type cranes it is imperative that the co-efficiency of these components are ensured as there is potential for ingress of foreign material which could cause slippage, e.g. water, grease etc |  |  |
| Overhoist Limits/Cut-outs |  |  |  |
|  | Function check of the boom minimum radius cut-out. The hook blocks (main/auxiliary) overhoist cut-outs. These checks should be extended to include maximum radius and maximum pay-out limits, when they are fitted |  |  |
| Rated Capacity Indicators -Safe Load Indicators) |  |  |  |
|  | the appropriate platform or sea state condition is selected Where a mechanically operated rated capacity indicator is in use, ensure that the correct platform/sea-state cam is fitted. . |  |  |
|  | the correct number of wire rope falls is displayed |  |  |
|  | Activate the test function to ensure that all visual and audible alarms operate correctly |  |  |
|  | Ensure that appropriate load/radius chart is in good condition and posted at a strategic point within the operator’s cabin. |  |  |
| Emergency Load Release and Gross Overload Protection System | Always ensure that the manually applied Emergency Load Release is secure and cannot be inadvertently activated during normal operations. This type of system, where fitted, must be function checked in controlled circumstances, generally with an unladen hook and only by a competent person who is authorised to perform the activity |  |  |
| Safety Equipment | Lifejacket and emergency escape equipment is secure and in good condition. Fire extinguishes are the correct type and size as specified by the Owner that they are familiar with application and use of the units provided. are in date and fully functional |  |  |