| No. | Description | Compliance (Yes/No | Observations / Findings | Action Required / Recommendations | Action required by | Due Date |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Does the activity have a valid work permit dedicated for grating activity, approved JSA (Job Safety Analysis) and STA (Safety Task Assignment) available and communicated? |  |  |  |  |  |
| 2 | Is a PMT approved method statement available and communicated to the employees involved in the task? |  |  |  |  |  |
| 3 | Do the team involved in the activity have a grating removal permit and checklist in place prior to the removal of the grating/floor plate/guardrail. |  |  |  |  |  |
| 4 | Where applicable is a lifeline installed for the activity with all necessary documentation available? |  |  |  |  |  |
| 5 | Have all employees involved in the activity been trained on Working @ Heights? |  |  |  |  |  |
| 6 | Do all employees practice 100% tie off? |  |  |  |  |  |
| 7 | Is a drop zone identified and barricaded with proper signage? |  |  |  |  |  |
| 8 | Are there dedicated watchmen assigned to control access into the danger zone? |  |  |  |  |  |
| 9 | Are tool bags supplied and used? |  |  |  |  |  |
| 10 | Are wrist lanyards supplied and used? |  |  |  |  |  |
| 11 | Is adequate and safe access/egress provided to the area of work? |  |  |  |  |  |
| 12 | After preparation for grating removal/installation activity does the supervisor /HSE team visit actual work location to confirms site condition? |  |  |  |  |  |
| 13 | Does the structure have suitable and safe access to the different platforms? |  |  |  |  |  |
| 14 | Is edge protection provided in the form of kick plates, mid rails and handrails? |  |  |  |  |  |
| 15 | Do all 4 sides of the grating panel rest properly on the supporting beams? |  |  |  |  |  |
| 16 | Are all grating panels secured with grating clips at each corner of the grating panel with no gaps in-between to avoid lateral movement? |  |  |  |  |  |
| 17 | Are grating stops on panel ends found smaller than the adjacent grating bearing spans ? Is there a potential for lateral grating movement.? |  |  |  |  |  |
| 17 | Are all grating bolts secured and tight? |  |  |  |  |  |
| 18 | Are gratings, bolts, clips free from corrosion? |  |  |  |  |  |
| 19 | Is the grating opening covered with a scaffold plank or other “approved” covers such as plywood, steel plates etc., that will withstand any imposed loads? |  |  |  |  |  |
| 20 | Are all covers on the opening properly secured? and is periodically inspected? |  |  |  |  |  |
| 21 | Does the grating openings properly barricaded with suitable signage? |  |  |  |  |  |
| 22 | Does the support beams provide underneath the grating hinge? |  |  |  |  |  |
| 23 | Does all the main structural members & roof structures installed in accordance with the Project Specification and drawings, and all the temporary aids/brackets removed? |  |  |  |  |  |
| 24 | Is the stacking of gratings to be installed or stacking of removed gratings done safely, without overloading the platform and to without potential trip/fall hazards, obstruction, etc.? |  |  |  |  |  |
| 25 | Are there lift bars or special tools used for the safe handling of grating during installation or modification? |  |  |  |  |  |
| 26 | Are there adequate numbers of workers assigned to handle each grating during installation/modification? Are the workers trained on the hazards? Are they aware that gratings weigh around 100Kgs and cannot be handled alone? |  |  |  |  |  |
| 27 | Is there a competent supervision monitoring the grating installation/modification activity from start to completion? Does the crew speak the same language or understands each other? |  |  |  |  |  |
| 28 | For structures where grating installations/modifications are not yet completed, is the access restricted with a hard barricade and provided with appropriate warning signs (Harness compulsory use)? |  |  |  |  |  |
| 29 | For structures where grating installations/modifications are completed, inspected and RFI-approved by Contractor and Company, is the appropriate “Safety Harness Free Zone” sign displayed? |  |  |  |  |  |
|  | Is RFI and inspection done at every stage of construction before allowing access to the platform instead of waiting until completion of the grating work. |  |  |  |  |  |
| 30 | Is there a register used to track down the number of open and closed work permits for grating installation; register to track down the number of gratings removed? |  |  |  |  |  |
| 31 | Is there an inspection process available after completion of grating installation? Is final grating inspection complete as per inspection plan (ITP and its stage inspection through RFI notification)? |  |  |  |  |  |
| 32 | Do the installation team have a mini fall protection plan available and is it discussed with the installation crew? |  |  |  |  |  |
| 33 | Is the necessary equipment available to rescue an employee should a fall occur? Is the emergency contact number displayed? |  |  |  |  |  |
| 3 | Grating penetrations for pipes, cables etc.., must have correct kick plate installed the be temporarily and safety covered. |  |  |  |  |  |
|  | Are Kicker plates installed without any offset and without any protrusion on access ways. |  |  |  |  |  |
|  | Is the handrails properly bolted and secured without any missing bolts ? |  |  |  |  |  |

Comments: