| Job Safety Analysis Sheet |
| --- |
| JOB DESCRIPTION: Erection & Use of Scaffolding | JSA Ref. No. JSA / KOC / 07 |
| Facility: | Work Area / Equipment: | Permit No. Date: |
| PERSONAL PROTECTIVE EQUIPMENT: Hard Hat, Safety Shoes, Hand Gloves, Safety Harness. |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | Yes / No | PRECAUTIONS |
| Pre – Work | Location of Emergency Equipment near the proposed Scaffolding |  | Ensure the emergency equipment will not be blocked or damaged due to scaffolding erection. |
|  | Non-compliance of KOC -HSEMS Procedures, F & S Regulations & Engineering Standards |  | Refer Chapter -13 of KOC F & S Regulations, HSEMS Procedure Doc. No. SA.KOC.002 ‘Control & Use of Scaffolding, & Recommended Practice KOC – L – 025 “Scaffolding” |
|  | Unauthorized erection of scaffolding |  | Obtain the Cold Work Permit. |
| Erection & Use of Scaffolding | Damage to onsite detectors / switches / transmitters etc |  | Take extreme care during erection and override it if needed. |
|  | Fall of objects / Tools. |  | Provide guardrail & toe board to prevent falling of tools / objects. Don’t keep the unnecessary materials on the scaffold platform. Hand tools to be tied with permanent structure or person. If required barricade the area during erection work. |
|  | Accidental Fall of Person |  | The Scaffolder must use Safety Harness to prevent accidental fall . |
|  | Unstable Scaffold |  | The scaffold must be inspected, certified & tagged by the competent person confirming its suitability. |
|  | Weak Scaffold |  | The scaffold tag must indicate the maximum load that it can bear. |
|  | Damaged Scaffold |  | The scaffolding is to be inspected at least weekly for any damage due to weather condition (rain, high wind etc) or other unsafe conditions. |
|  | Modified Scaffold |  | In case of any modification, addition in the scaffold, it has to be re-inspected & certified. |
|  | Improperly Supported Scaffold |  | Ensure Scaffold is securely supported on a rigid ground and not on process piping / vessel or equipment. |
|  | Incomplete Scaffold |  | Do not use if green Tag is missing. Do not use if red tag is available. |
| Old Scaffolding | Doubtful Integrity |  | Do not use if it does not have valid inspection tag attached. |
| Additional Hazards (Other than indicated above) |  |  |
| JSA Done By | Name: Designation: KOC / ID. No. Company: Controlling Team: Contract No.(If Applicable): Signature: Date: |