| Job Safety Analysis Sheet |
| --- |
| JOB DESCRIPTION: Removal of Scaffolding | JSA Ref. No. JSA / KOC / 10 |
| Facility: | Work Area / Equipment: | Permit No. Date: |
| PERSONAL PROTECTIVE EQUIPMENT: Hard Hat, Safety Shoes, Hand Gloves, Safety Harness. |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | Yes /No | PRECAUTIONS |
| Pre – Work | Location of Emergency Equipment near the Scaffolding |  | Ensure the emergency equipment will not be accidentally hit or damaged due to scaffolding removal. |
|  | Non-compliance of KOC -HSEMS Procedures, F & S Regulations & Engineering Standards |  | Refer Chapter -13 of KOC F & S Regulations, HSEMS Procedure Doc. No. SA.KOC.002 ‘Control & Use of Scaffolding, & Recommended Practice KOC – L – 025 “Scaffolding” |
|  | Unauthorized Removal of scaffolding |  | Obtain the Cold Work Permit |
| Dismantling of Scaffold | Damage to onsite detectors or switches |  | Take extreme care during removal and override it if needed. |
|  | Fall of objects / Tools. |  | Take proper care while dismantling the scaffold to prevent fall of scaffold parts. Hand tools to be tied with permanent structure or person. Use proper PPE during removal of scaffold. If required barricade the area during dismantle work. |
|  | Accidental Fall of Person |  | The Scaffolder must use Safety Harness to prevent accidental fall . |
|  | Unstable Scaffold |  | Inspect the scaffold for its stability & support before removing in sequence. . |
|  | Loaded Scaffolding |  | Remove safely the load / equipment / plant from the scaffold before dismantling the scaffold. |
|  | Damaged Scaffold |  | The scaffolding is to be inspected for any damage before dismantling. Take extreme care while removing a loose part / attachment from the scaffold. |
| Housekeeping | Scattered Materials |  | Arrange the dismantled parts of the scaffold and stack properly. Segregate different parts of scaffold and store it separately. |
|  | Defective Part |  | Remove and discard the defective parts / attachment from the scaffold storage. |
| Additional Hazards (Other than indicated above) |  |  |
| JSA Done By | Name: Designation: KOC / ID. No. Company: Controlling Team: Contract No.(If Applicable): Signature: Date: |