| Project No. | W912ER-04-D-0004-0022 | Task Order/Contract No.: | Task Order 22 | Date: | Jan - 07 - 2011 |
| --- | --- | --- | --- | --- | --- |
| Prepared By: | Laith Shaker |
| Company Name: | Fluor Govermant group |
| Building: | Base Wide | Area: | Victory Base Complex IRAQ - BAGHDAD |
| Work Scope/Description: Working on Ladders and Scaffolding |
|  | Primary | Project HSE |
| Emergency Contact Person(s): | Harold Penley | Harold Penley |
| Emergency Radio/Phone No.: | Radio Call Safety 1 | 814 - 546 - 5969 |
| Specific Work Location(s): All Work Locations - This is a general Job Safety Analysis |
| Pre-Task Walkthrough Conducted: | Yes | No | HSE Program Reference (***): | Corporate/000 | Project-Specific |
| KNOWN OR POTENTIAL HAZARDS |
|  | Yes | No |  |  | Yes | No |  |
| 1. Radiation Area Work | ( | ( |  |  |  | ***.653.2300/RWP | 17. Respiratory Hazards | ( |  |  |  |  | ***.653.3002 |
| 2. Hazardous Waste Operations | ( | ( |  |  |  | 29 CFR 1910.120 | 18. Noise Exposure | ( |  |  |  |  | ***.653.3003 |
| 3. Confined Space | ( | ( | ( |  |  | ***.653.3322 | 19. Temperature Extremes |  |  |  |  |  | ***.653.2000/2003 |
| 4. Hot Work | ( | ( |  |  |  | ***.653.3101 | 20. Hoisting & Rigging | ( |  | ( |  |  | ***.653.3201 |
| 5. Roof Work |  | ( | ( |  |  | ***.653.3304 | 21. Repetitive Motion |  |  |  |  |  | ***.653.2009 |
| 6. Fall Hazards (> 6 ft) | ( | ( | ( |  |  | ***.653.3001 | 22. Awkward Positions |  |  |  |  |  | ***.653.2009 |
| 7. Excavation/Trenching |  | ( | ( |  |  | ***.653.3311 | 23. Same Position(s) |  |  |  |  |  | ***.653.2009 |
| 8. Ladders and Scaffolding | ( | ( | ( |  |  | ***.653.3302/3203 | 24. Biological/ Vermin |  |  |  |  |  | ***.653.2101/2103 |
| 9. Aerial Lifts | ( |  |  |  |  | ***.653.3204 | 25. Insects/ Varmints |  |  |  |  |  | ***.653.2102/2103 |
| 10. Heavy Equipment | ( |  | ( |  |  | ***.653.3200 | 26. Signs and Barricades |  |  |  |  |  | ***.653.3301 |
| 11. Lock and Tag | ( | ( | ( |  |  | ***.653.3315 | 27. Sharp Objects |  |  |  |
| 12. Site/Vehicle Traffic |  |  |  |  |  | ***.653.3211 | 28. Hexavalent Chromium |  |  | ***.653.2011 |
| 13. Electrical Hazards | ( | ( | ( |  |  | ***.653.3309 | 29. |  |  |  |
| 14. Asbestos Work | ( | ( | ( |  |  | ***.653.2006 | 30. |  |  |  |
| 15. Lead Work | ( | ( | ( |  |  | ***.653.2005 | 31. |  |  |  |
| 16. Hazardous Materials/MSDS | ( |  |  |  |  | ***.653.3102 | 32. |  |  |  |
| (= Requires formal/special training | 33. |  |  |  |
| ( = Requires a permit/form/report | 34. |  |  |  |
| ( = Requires certification or Competent/Qualified Person designation | 35. |  |  |  |
| Error Precursors: Identify all that may be applicable to the job. |
| Task Demands | Individual Capabilities |
|  | Time pressure (in a hurry) |  | Unfamiliarity with task – first time |
|  | High workload (memory requirements) |  | Lack of knowledge (mental model) |
|  | Simultaneous, multiple tasks |  | New technique not used before |
|  | Repetitive actions, monotonous |  | Imprecise communication habits |
|  | Irrecoverable acts |  | Lack of proficiency/inexperience |
|  | Interpretation requirement |  | Indistinct problem-solving skills |
|  | Unclear goals, roles, and responsibilities |  | “Hazardous” attitude for critical task |
|  | Lack of or unclear standards |  | Illness/fatigue |
| Work Environment | Human Nature |
|  | Distractions/interruptions |  | Stress (limits attention) |
|  | Changes/departures from routine |  | Habit patterns |
|  | Confusing displays or controls |  | Assumptions (inaccurate mental picture) |
|  | Workarounds/OOS instruments |  | Complacency/overconfidence |
|  | Hidden system response |  | Mindset (“turned” to see) |
|  | Unexpected equipment conditions |  | Inaccurate risk perception (Pollyanna mindset) |
|  | Lack of alternative indication |  | Mental shortcuts (biases) |
|  | Personality conflicts |  | Limited short-term memory |
| SPECIFIC HAZARD ANALYSIS AND SAFE WORK REQUIREMENTS |
| Known and/or potential hazards, including any marked “yes” above, are further evaluated, and specific measures are identified on subsequent pages. This discussion must include identification of the work activity, the specific hazards present, and the safe work requirements/controls (including a hazards assessment/modification for PPE) to be used to alleviate/control the hazard(s). |
| MINIMUM DRESS/PPE REQUIREMENTS: Hard Hat, Safety Glasses, Substantial Footwear, Long Pants, Shirt with Sleeves |
| Supervisor |  | Date |  | HSE Representative |  | Date |  | Industrial Hygiene |  | Date |
| Walkdowns |
|  | Walkdowns are completed in advance of the work. |
|  | Ideally, this review includes walkdown by the employees who will actually perform the task. |
|  | During the walkdown, the work scope is validated and verified, including materials and special tools needed to complete the task. |
|  | The walkdown should consider environmental and workplace factors that may impact critical steps of the task. |
|  | The consistency and thoroughness of walkdowns are improved with the aid of a checklist. |
|  | Use the walkdown as an opportunity to observe physical limitations that may exacerbate performance, especially at the critical steps, or hinder execution. |
|  | The results of the walkdowns are incorporated into work packages or documentation preparation. |
| Safety Task Assignment |
|  | Qualification for the task is first and foremost, but not the only, consideration. |
|  | Assigning the right employee to the task is an opportunity for the supervisor to evaluate the risk, complexity, and frequency of performance of the task. |
|  | Experience, proficiency, personal readiness, and previous risk-taking behavior should be considered in light of the risk and complexity of the task, as well as how often task has been performed. |
|  | Factors related to an employee’s mental, physical, and emotional readiness to work should be considered such as fatigue, illness, emotional stress, and physical disabilities relevant to the task. |
| Pre-Task Briefings |
|  | Employees should be given the opportunity to talk about what is to be accomplished and what should be avoided. |
|  | Possible negative consequences should be discussed to identify additional controls or barriers needed. |
|  | The supervisor and the employee can develop contingencies for the most likely and worst-case outcomes. |
|  | Such thinking enhances situational awareness and improves application of error-prevention tools at critical points in a task. |
| Work Activity | Hazards Present | Required Safety Measures/PPE |
| Activity Hazard Analysis | None | AHA shall be submitted, accepted and signed by USACE GRC Representative prior to work starting. AHA shall be reviewed, accepted and signed by Site Manager prior to work starting. AHA shall be reviewed and signed by each employee that will work on this project – prior to the employee starting work – no exceptions |
| Safety Task Assignment | None | STA shall be prepared by supervisor or appointed person prior to start of work or task STA shall be reviewed with each employee working on the task – prior to that employee beginning work. STA shall be signed by each employee acknowledging that he/she understands and will abide by the procedures that are outlined. STA shall be signed by each employee when he/she completes their task and has finished the job. STA shall be reviewed, during the work day, by the supervisor to ensure that all topic and hazards have been covered and documented. STA shall be returned to the HSE Department at the end of the day for logging into the data base. |
| Signs and Barricades | Falls, Trips, Slips, Unauthorized Entry, etc… | All safety signs and barricades shall be written in both English and Arabic. Signs and Barricades for Electrical Hazards and other HSE issues shall be put in place before the work begins for identification of hazards in the work area. The following are a few examples of proper signs and barricades but no limited to: Caution – yellow barricade tape DO NOT ENTER – red barricade tape Overhead Hazard LOTO Open Hole Equipment Under Commissioning Site Traffic Directions PPE Required in this Area |
| Housekeeping in Work Area | Slips, Trips and Falls | Supervision and workers shall insure that the work area has clear access to and from the site, walkways clear of debris and area clear of housekeeping hazards before work begins. Work surface and work area shall be maintained in an orderly fashion throughout the work day. All hazards that could result in slips or trips shall be removed or marked. These materials or an other that can cause injury shall be removed from the work area Housekeeping is everyone’s responsibility and shall be an ongoing process Housekeeping shall bin in accordance with Fluor Health and safety Manual and USACE EM 385-1-1. |
| General Work | Hazards to the Head, eyes, ears, nose, torso, hands, feet, etc… | PPE is required for all employees working on this project. The following is a list of items that are to be worn – additional PPE requirements will be addressed on a as needed basis: Hard Hat Safety Glasses Hearing Protection Face Shield Safety Goggles Welding Hood Proper Work Clothing Hand Protection – gloves of various types Work Boots or Work Shoes Proper storage and upkeep of the PPE is required according to manufacture and project standards. All PPE that is worn shall be in compliance with Fluor Safety and Health Manual ,HSE # 000-653-3000, |
| Working on scaffolding to perform the intended work | Falls. scaffold collapse, serious injury, Death, property damage etc... | Scaffold components and connections shall Be in good condition and secure. Scaffold is to level and plumb resting on base plates, supported scaffold and a firm foundation is Required. ( cross bracing/equipments) are installed between scaffold legs, and scaffold to be constructed to support the maximum Intended load. Tubular scaffolds are the Type used in this project. Only designated competent Persons are to direct scaffold selection and erection/dismantling, inspect scaffolds, train scaffold erectors, inspectors and maintenance/repair persons, Training shall be documented. Only trained employees shall erect, maintain, inspect, use, dismantling, scaffolds, those will be documented as scaffold trained User’s erector, inspector etc... training shall be provided by a Competent person. Training standards, scaffolds requirements, type of the scaffolds, and scaffold's components material shall be in compliance with health requirements manual * FGG health safety, and environmental program - Practices #000 653 3302 scaffold - Practice #000.653.3001 fall protection - Practice # 000 653 3009 Electrical work safety. Scaffolds to be utilized only for their intended purpose there components shall meet the requirements of ANSI A10.8 and be capable of supporting, without failure, their own weight and at least 4 times the maximum Anticipated load. |
| Working on Scaffolding to perform the intended work | Falls. Scaffold collapse, serious injury, death, property damage etc... | Construct tubular scaffolds and equivalent scaffolds with knowledge of the maximum intended load and in accordance with the design criteria and the Manufacture’s recommendations. Ensure that the scaffold is plumb and level, and that supported scaffold poles, legs, pots, frames and uprights bear on base plates and mud sills or base plates and other adequate foundation such as concrete slab flooring Where a scaffold's height exceeds 4 times its smallest base dimension, guy, tie, or otherwise brace the scaffold at the closest horizontal member to the 4:1 Height. Repeat every 7.9 meters (26 feet) vertically. DO not modify or remove a scaffold system/component or Scaffold status tag. Scaffold is damaged, wreaked, or otherwise Deficient. Report and document That immediately. When erecting or dismantling scaffolds, commence using safety harnesses and lanyards at the 6- foot working level ( Full body harness to be utilized as stated in fall protection-general AHA). Place scaffolds as close to the Work as possible. If fall protection is provided by the structure on which the work is being performed (such as a building or wall), allow no more than 350 millimeters (14 inches) between the scaffold platform and the structure Red, yellow, and green tags to be utilized to show scaffold status near the access point of any scaffold being used, erected, or dismantled Work only from scaffolds having a completed yellow or green scaffold status tag and a current Scaffold inspection tag affixed. Comply with special conditions/additional controls Noted on the tag(s). |
| Erecting scaffoldings. and access | Electrocution. Other electrical hazards | Check the clearance distances listed in the standard according to the FGG practice #000 653 3009 Scaffolding shall not be erected near power lines (Min 10 feet or 3 meters From all & power lines) |
| Erecting scaffoldings, working on Scaffolding. | Falls from elevation – caused by slipping, unsafe access, and the lack of fall Protection. Struck by falling tools/debris | If workers on a scaffold are expose to fall hazards more then 1.8M/6feet, protect them from falls using a positive means of fall Protection-and safe access. Fall protection to be provided in according to FGG health safety, and environmental program and Fluor practices and #000653.3001 for conducting training, erecting, working on, inspection, disassembling scaffolding where Employee exposes to fall hazards. Training shall be conducted by a competent person, and Documented. Scaffolds guard rail to be: Install along open sides & ends Front edge of platforms not more than 14 in. (35 cm) from the face of the building Top rails – 42 in. +/- 3 in. (107cm) height Mid rails halfway between top rail and platform Toe boards at least 4 in. (10 cm) High. Capable of withstanding, without failure, a force of at least 90 kg (200 lbs) applied within 5 vm (2 in) of top ledge, in any outward or downward direction, at any Points along the edge. Dimensions and materials of guardrail components shall be in compliance with the standard of FGG health safety environmental practice # 3001 Do not straddles, stand on, or work outside The guardrail. |
| Erecting scaffoldings, working on Scaffolding. | Struck by falling objects | Install protection (such as toe boards, netting, and/or fencing) where employees located on or below a scaffold are expose to the possibility of objects falling from Overhead. More options for protection like: Mark or post scaffold areas with warning flags or barriers where Vehicular traffic is present. Barricade area below scaffold to forbid entry into that area is Another option. Use panels or screens if material is Stacked higher than toe board. Build a canopy or erect a net below the scaffold that will contain or deflect falling objects. |
| Erecting scaffoldings, access to the scaffold, Working on scaffolding. | Fall hazards and other serious injuries. | When scaffold platforms are more than 0.6 meter (2 feet) above or below a point of access ensure that scaffolds are providing with stable access. Use only approved access means to ascend and descend scaffolds (stairs, attached ladders, or specially designed end frame); do Not uses cross bracing or side rails. Portable ladders, hook on ladders, attachable ladders, stair tower, ramps, walkways, integral prefabricated scaffold access, or direct access from another scaffold, structure, personnel hoist, or similar approved surface are Used. Installation and use of ladders shall be conforming to ANSI A14.1, ANSI 14.2 ANSI A14.3 as applicable. Only methods approved by the manufacturer and in compliance with the safety requirements of the USACE EM 385-1-1 safety and health requirements manual, and FGG health safety and environmental program are used to provide a safe transition from the access point to the scaffold’ platform and to maintain the integrity of the scaffold's guardrail System. Method and training shall be in compliance with the USACE EM 385-1-1 safety and health requirements manual and FGG health safety and environmental program – practice # 000. 653 3302/3202 |
| Erecting scaffoldings, access to the scaffold, Working on scaffolding. | Fall from elevation when scaffold platforms or planks fail | Platforms must: be fully planked or decked with no more than 2.5 cm (1”) gaps be able to support its weight & 4 times maximum load be at least 45 cm (18”) wide No large gaps in front edge of platforms Each abutted end of plank must rest on a spear support surface Overlap platforms at least 30 cm (12”) over supports, unless restrained to prevent movement No paint on wood platforms Use scaffold grade wood Fully planked between front upright and guardrail support Component pieces used must match and be of the same type Erect on stable and level ground Each end of a platform, unless cleared or otherwise restrained by hooks, must extend over its support by at least 15 cm (6”) |
| Erecting scaffoldings, access to the scaffold, working on scaffolding. | Fall, scaffolding collapse ect.... | Inspect and use only approved and appropriate constructed scaffolds which are in compliance with the safety standards of USACE EM 385-1-1 safety and health requirements manual, ANSI A10.8 , and FGG health, safety, and environmental program Use mobile scaffolds only on firm, level surfaces, Lock the casters or wheels before using mobile Scaffolds. No employee can be on scaffold 'platform while it is moved. Employees can't be on scaffold part beyond the wheels Scaffolds to be supported by legs, outrigger beams, brackets, poles, uprights, posts, & frames, and uprights must be on base plates and mud sills or other firm foundation |
| Roof platform access, and work performed via portable ladder | Fall hazard | Installation and use of ladders shall be Conforming to ANSI A 14.1, ANSI 14.2 ANSI A14.3 as applicable. 1- All portable ladders shall be of sufficient length and shall be places so that workers will not stretch or assume a hazardous position. 2- Portable ladders used as temporary access shall extend at least 3ft (.09M) above the upper landing surface. 3- in no case shall the length of the ladder be such that ladder deflection Under a load would, by it self, cause ladder to slip from its support. 4- Ladder shall not be placed in passageways, doorways, drivers, or any location where they may be displaced by any other work unless Protected by barricades or guards. 5- Portable ladders shall be used at such pitch that the horizontal distance from the top support to the foot of the ladder will not be greater then one – fourth the vertical distance between these Points. 6- Ladders shall be secured by top, bottom, and intermediate fasting as required to hold the rigidly in place and to support the loads that will be Imposed upon them. 7- No work requiring of heavy material or substantial exertion shall be done from ladders. 8- Ladders shall not be moved, shifted, extended while occupied. 9- Ladders shall be inspected for visible defects on a daily basis and after an occurrence that could affect their safe Use. 10- Broken and damaged ladders shall be immediately tagged “ DO NOT USE” and withdrawn from service until restored to a condition meeting their original design. 11- Ladders shall be restricted to their intended use. 12- Ladders shall not be climbed by more than one person at a time unless it is designated to be climbed by more than one person 13- Maintain three points contact with ladder while climbing or being on the Ladder. Utilizing ladder shall be in compliance with FGG health safety an environmental program practices # 000.653.3302,/3202. |
| Inspection (ladders. And scaffolds) | Fall hazards. scaffold collapse and frailer. Different injuries. | Only trained employees shall conduct the inspections. All required protection measures to be provided when inspect scaffoldings. Daily and routine inspections procedure required and shall be conducted and documented according to the USACE EM 385-1-1 and FGG health safety andenvironmental program. |

Note:  This form is referenced in numerous practices.