# RISK ASSESSMENT - SHEET 2

# QAD 210.13.14

# TASK ANALYSIS SCHEDULE

| Task Code | Involved Personnel |  |  |
| --- | --- | --- | --- |
| T25 |  |  |  |
|  | Scaffolders – Fabrication Personnel – On site Contractors – Site Visitors |  |  |
| Scaffolding |  |  |  |
| Erection and | PO = PROBABILITY OF OCCURRENCE - RISK LEVEL = HIGH (H) - MEDIUM (M) - LOW (L) |  |  |
| Dismantling | CO = CONSEQUENCE OF OCCURRENCE - RISK LEVEL = HIGH (H) - MEDIUM (M) - LOW (L) |  |  |
|  | Note that should an H – High PO and an H – High CO be recorded together for a risk exposure, the risk is unacceptable and further control measures are required. |  |  |
| Risk Exposure | Control Measures | PO | CO |
| Faulty or inadequate erection - Caused by a lack of information as to the intended use of the scaffold once completed. Or the erection not being performed within the relevant codes of practice. | Assessment shall be made by supervisors and/or responsible persons to establish the proposed use of the scaffold, taking into account numbers of personnel, plant and equipment ETC. which will require support. Erection shall be performed in line with current approved codes of practice. Scafftags shall be placed at every access point to the scaffold detailing the intended use of the scaffold. The scaffold structure shall be inspected every seven days or after being exposed to high winds and the scafftag re-validated by the appointed scaffolding inspector. |  |  |
|  |  | M | H |
| Falls of equipment – Scaffold poles and clips etc. can fall easily if not adequately secured during the erection process. | Care shall be taken to ensure suitable means of manoeuvring equipment during the erection process are implemented by using mechanical equipment where possible. The surrounding area shall be barriered off to restrict access into the work zone. Scaffold platforms shall be fitted with double handrails and toe boards. |  |  |
|  |  | M | H |
| Falls of personnel – can occur if personnel overbalance, slip or loose their grip when erecting or dismantling scaffold. | PPE shall be worn at all times, such as full body safety harness and enertia reels etc. |  |  |
| Continued on next page. |  |  |  |
| Risk Exposure | Control Measures | PO | CO |
| Continued. | Only nominated and qualified scaffolders shall erect, alter or dismantle scaffolding. |  |  |
|  |  | M | H |
| Injury from jagged ends of scaffold tubes – this can occur when lengths of tubes are cut. | Jagged ends shall be protected by end caps or taped with masking tape etc.. |  |  |
|  |  | M | L |
| Adverse weather conditions – such as high winds, rain, snow and frost. | Suitable judgement to be made by safety department whether scaffolding can be worked on in high winds. Suitable clothing shall be worn during erection/dismantling to protect the body from adverse conditions. |  |  |
|  |  | L | H |
| Scaffold collapse – can occur if scaffold is not dismantled in a safe manner, taking into account stresses on the scaffold and main supports and ties etc. | Scaffolds shall only be erected and dismantled by authorised scaffolders, no other persons shall alter scaffold in any way or form. The area around the scaffold to be barriered off to prevent access to unauthorised personnel. Tool box talk shall be held by scaffold squad to establish responsibilities during the dismantling process. |  |  |
|  |  | L | H |
| Injuries from handling scaffold equipment etc. – hand injuries can occur during the handling of scaffold equipment. Manoeuvring boards in high winds can cause loss of balance. Plant and equipment can be damaged when struck by scaffold equipment being moved. | Suitable gloves to be worn when handling scaffold equipment. Weather conditions to be considered when erecting, dismantling or moving scaffold equipment. Mechanical means to be used to move scaffold equipment whenever possible. Dual handling shall be used when possible to reduce the risk of injury. |  |  |
|  |  | M | M |

# Risk Assessment carried out

for Heerema Hartlepool :		Date : __________	Signature : ____________________

| Lead Assessor | Name | D. Gorman | Job Title | SHE Officer |
| --- | --- | --- | --- | --- |
| Assisted by | Name | B. Yeoman | Job Title | Production Manager |
| Assisted by | Name | W. Hegarty | Job Title | Superintendent |
| Assisted by | Name | P.J. Quayle | Job Title | Q.A. / Environmental Engineer |
| Assisted by | Name | E. Jackson | Job Title | Safety Representative |