| Task: Erect scaffolding for work on Crane ‘A’ frame |
| --- |
| Elements: Scaffolding, riggers, welders |  |  |
| Hand tools. |  |  |

Competent person(s) to carry out task: Scaffolders, Welders, Crane Op, Asst. Crane Op, Deck Crew

Competent person(s) to carry out risk assessment: Scaffold Foreman, Welder, Barge Supv., Crane Op. RSTC

| Task steps | Hazard | Who or what | Existing controls/safeguards | Risk | Additional controls/safeguards | Risk |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Per. | Env. | Prop. |  | S x | P = | R |  | S | P | R |
| Erecting scaffolding | Falling from partially built scaffold on to deck or into the water Fatality or injury. Also possibility of drowning. Being struck by objects falling from above Failure of scaffolding equipment (Batons) | X |  | X | Permit to work, safety harness and inertia reels to be used at all times, only competent personnel to erect scaffold, proper PPE to be worn, stand by watch man with Radio to maintain communication with Radio room, Radio operator to check on the closest Boat to the Rig to be by. Non essential personnel to stay clear of work site. Good communications. All hand tools to be tied off. All equipment used must be in good condition. | 3 | 2 | 6 | Standby watchman to be in radio contacts with either Radio room or with the standby vessel and if it's available at all times. Risk assessment to be read and understood. Observing weather condition – Wind Speed. Certification of equipment. | 3 | 1 | 3 |
| Lifting equipment up to scaffolding platform | Dropped object whilst lifting | X |  |  | Correct rigging and lifting techniques as per LOLER regulations. Only competent personnel to rig up lifting equipment for task. Non essential personnel to keep clear of area, warning by barriers and PA system | 4 | 1 | 4 | Barriered tape to erect around the area underneath. | 4 | 0 | 0 |
| Fitting equipment as specified in work scope | Dropped object from hand tools | X |  |  | Hand tools must be secured at all times to prevent a dropped object. | 4 | 1 | 4 | Barriered tape to erect around the area underneath. | 4 | 0 | 0 |
| Welding operations as specified in work scope | Burning and grinding flying objects | X |  |  | Firewatcher posted, correct PPE, non essential personnel to stay clear of area. Only suitably qualified welder to carry out work. | 3 | 2 | 6 | Barriers erected around scaffolding to prevent flying objects falling to deck | 3 | 1 | 3 |
|  |  |  |  |  |  | 6 |  | 3 |

Comments and Conclusions:

Risk Assessment team members:

| Name | Position | Signature | Date |
| --- | --- | --- | --- |
| K. Ridings | OIM |  | 25-May-06 |
| Sherin Fouad | RSTC |  | 25-May-06 |
| Medhat Hassan | B.Supv |  | 25-May-06 |

Reviewed by OIM:

| Name | Comments | Signature | Date |
| --- | --- | --- | --- |