Scaffolding Safety Checklist

| Yes | No | Action(if no) |
| --- | --- | --- |

| # | GENERAL REQUIREMENTS |
| --- | --- |
| 1 | Is the scaffold being erected under the direction of a competent person? |  |  |  |
| 2 | Is the footing sound and rigid - not set on soft ground, frozen ground (that could melt), or resting on blocks? |  |  |  |
| 3 | Has the erection site been evaluated for hazards such as earth fills, ditches, debris, underground electric wires, unguarded openings, or conditions created by other trades? |  |  |  |
| 4 | Are wheels / castors locked? |  |  |  |
| 5 | Is the scaffold able to hold four times its maximum intended load? |  |  |  |
| 6 | Are guardrails and toeboards in place on all open sides? |  |  |  |
| 7 | Is the platform complete front to back and side to side (fully planked or decked, with no gaps greater than 1 inch)? |  |  |  |
| 8 | Is the lumber free of cracks, splits, knots, or damage? |  |  |  |
| 9 | Is the scaffold level? |  |  |  |
| 10 | Have all compounds been inspected for defects such as broken welds, corroded members, and missing locks, bent or dented tubes? |  |  |  |
| 11 | Are all braces, bearer, and clamps secured all sections pinned or appropriately secured? |  |  |  |
| 12 | Is there a safe way to get on and off the scaffold, such as a ladder (without climbing on crossbraces)? |  |  |  |
| 13 | Is the front of the scaffold within 14 inches of the work? |  |  |  |
| 14 | Does the scaffold meet electrical safety clearance distances? |  |  |  |
| 15 | Is the scaffold under 125 feet in height? |  |  |  |
| 16 | Is the "X" bracing installed on the ends of the scaffold and every third set of post horizontally and every fourth vertical runner? |  |  |  |
| 17 | Are severe weather provisions in place i.e. during high winds, rain, snow, or bad weather? |  |  |  |
| 18 | Have all planks been properly secured to the scaffold structure to prevent them blowing off in the event of high winds? |  |  |  |
| 19 | Where persons work under scaffold, is a 1/2 inch mesh screen provided between toeboard and guard rail or has the area below the scaffold been cordoned off? |  |  |  |
| 20 | Are tag lines available for items to be loaded on to scaffold? |  |  |  |
| 21 | When employees are working on suspended scaffolds, are lifelines firmly anchored to an overhead structure and not to the scaffold? |  |  |  |
| 22 | Is the scaffold over 10 feet high, (if yes) is personal fall protection available, or are guardrails in place? |  |  |  |
| 23 | Are guardrails 38 inches high? |  |  |  |
| 24 | Are toeboards in place and at least 4 inches high? |  |  |  |
| 25 | Are midrails or equivalent in place? |  |  |  |
| 26 | Does the scaffold have a height to base ratio of at least 4:1? |  |  |  |

Job Competent Person: ____________________________________

Inspected By: ____________________________________________

Signature: ______________________ Date:____________________