11.2 Scaffolding

• Conditions:

􀂃 Scaffolding/Work Platforms <6 ft in height – AHA is required; plan is optional

􀂃 El CONCORDE shall inspect and approve all Temporary Works after erection and before access, loading or use is allowed. Completed and approved Temporary Works shall be tagged with a scaff-tag or similar safety system and the Safe Structure insert displayed. For scaffolding, one tag shall be displayed every 32 m2 of face area. A central record system shall be kept on all Temporary Work. Temporary Works shall be inspected weekly and similarly recorded.

􀂃 All mobile scaffold towers shall be erected in accordance with the manufacture's instructions.

Additionally, all towers shall be erected complete with access ladder, safety rails and kick boards whatever the height.

􀂃 El CONCORDE shall repair or replace, immediately, any scaffold including accessories, damaged or weakened from any cause.

􀂃 The Contractor shall ensure that any slippery conditions on scaffolds are eliminated as soon as possible after they occur.

􀂃 All scaffolds used for storing materials, for brick or block laying, for access to formwork or for any other purpose where materials may accidentally fall, shall be provided with wire mesh guards or guards of a substantial material, in addition to kick boards.

Use of Ladders

􀂃 Manufactured ladders shall meet the applicable safety codes for wood or metal ladders. Metal ladders shall not be used where there is any likelihood of contract with electric cables and equipment. All metal ladders shall be clearly marked: "Caution -Do not use around electrical equipment".

􀂃 Job made ladders shall not be permitted.

􀂃 Ladders rungs and steps shall be kept clean and free of grease and oil.

􀂃 Extension and straight ladders shall be tied off at the top and/or bottom when in use.

Only one person shall be allowed on a ladder at a time.

􀂃 Defective ladders shall be taken out of service and not used. Ladders shall not be painted and shall be inspected for defects prior to use.

􀂃 El Concorde will keep Fall Arrest Equipment and Safety Nets in a good condition and any damage will be the responsibility of El Concorde.