SIMPLE LIFT CHECKLIST

YES  /  NO

| 1 Do you know the weight of the load and does the lifting operation appear to be straight forward? |  |  |
| --- | --- | --- |
| 2 If the load is particularly heavy, do you have the relevant permit? |  |  |
| 3 Is there a crane or certified support steelwork (e.g. runway beam or lifting eye) directly above the load? |  |  |
| 4 Does the load have certified lifting points (lifting eyes/collar eyebolts etc) fitted and if not, can slings be wrapped around easily (e.g. no sharp edges, load not fragile etc)? |  |  |
| 5 Is there ample headroom for the lifting appliance and slings? |  |  |
| 6 Is the lift stable (e.g. centre of gravity below lifting points)? |  |  |
| 7 Is the lift balanced (e.g. centre of gravity in the middle) or fitted with special slings to compensate? |  |  |
| 8 Is the load free to be lifted (e.g. sea fastenings released, all hold-down bolts removed, not jammed etc)? |  |  |
| Is the removal routes suitably controlled/cordoned off and clear of any obstructions? |  |  |
| 10 Can the removal (lift, transfer and landing) be performed without cross-hauling? |  |  |
| 11 Is there a suitable laydown area and does the load come within the allowable load bearing (laydown) capacity of the deck? |  |  |
| 12 Are you experienced in using all the lifting equipment and gear involved and do you have a Rigging and Lifting Handbook? |  |  |

If the answer “yes” to all the above, proceed with the lift.

Assessment performed by 		Date

If the answer to any of the above is “no”, check with your immediate supervisor.

Note to Supervisors: If you can give solutions to the above negatives to allow the lift to proceed safely, write the instructions in the box below and if you cannot supply a solution, seek guidance from the appropriate competent person(s).

Solutions to overcome the above problems

Assessment approved by *		Date

* This shall be person who has completed Transocean (or equivalent) Rigging and Lifting course.